## Slide 1: SmartCard Lab - Final Presentation Group 3
Team 1:
Faraz Bhatti
Lu Yongchen
Mao Kaiyi
Team 2:
Christoph Wittmann
Yizhou Liu

## Slide 2: Content
Improvements on AES
Speed up attacking script
Pseudo Random Number Generator
Implemented countermeasures
  Hiding
    Dummy Operations
    Shuffling
  Masking
  True Random Number generator
  Benchmark
  Conclusion

## Slide 3
Improvements on AES - matrix multiply lookup tables
Since this math is done in 28 field, the addition above is actually an exclusive or operation, and multiplication is a complicated operation.

## Slide 4: Improvements on AES -- matrix multiply lookup tables
The processing time has been improved significantly.
Instead of the complicated math calculation, we defined the look-up tables for inverse MixColomns
For example: Lookup table for multiplying by 9
//0 1 2 3 4 5 6 7 8 9 A B C D E F
0x00, 0x09, 0x12, 0x1b, 0x24, 0x2d, 0x36, 0x3f, 0x48, 0x41, 0x5a, 0x53, 0x6c, 0x65, 0x7e, 0x77,
0x90, 0x99, 0x82, 0x8b, 0xb4, 0xbd, 0xa6, 0xaf, 0xd8, 0xd1, 0xca, 0xc3, 0xfc, 0xf5, 0xee, 0xe7,
…

## Slide 5: Script Speed Up Using Multiprocessing
-Amdahl's Law
-Parallel Part and Sequential Part of The Script
-Pool of Processes
-Spawning Processes
-Up to 3x Faster Processing

## Slide 6: Random Number Generator
XOR SHIFT PRNGs:
Input is a linear function of the previous state.
PRNG Tests:
Entropy Test :7.099790 bits per byte

## Slide 7: Hiding
Dummy Operation
Shuffling

## Slide 8: Hiding (Dummy Operations) Implementation
- Random misalignment of the AES operations in the time domain.
- Insert NOP operations so that the traces are not aligned in order to do compression or DPA attacks.
- The sum of operations should be the same in the end
- Total Number of Operations allowed – random()
- Last Count for NOP operations = remaining operations count.
- DPA Attack is not effective anymore
- 0 Correct Key Bytes

## Slide 9: Hiding( Dummy Operation ) Resultant Power Traces

## Slide 10: Power Trace Analysis

## Slide 11: Attacking Dummy Operations using MSE (Mean Squared Error)
Resultant Trace After Preprocessing
Then we perform simple 1st Order DPA Attack on this Trace .
And got correct key with 800 Traces in 72 seconds.

## Slide 12: Shuffling
Focusing on inverse SubByte
Using random numbers to determine the sequence of 16 S-box look-ups
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
4 | 8 | 12 | 16
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
After Shuffling
15 | 2 | 10 | 3 | 9 | 14 | 16 | 8 | 13 | 4 | 6 | 1 | 5 | 11 | 7 | 12
Mixed the sequence of SubByte
Hard to apply DPA attack

## Slide 13: Attacking on shuffling
If we take enough sample traces, and then for every single byte during the process, it should appear at the correct place several times. Thus we can still get the intermediate value correctly.
In phase 1,
500 traces
Correct key
After shuffling,
with 10000 traces
183 seconds

## Slide 14: Masking
In a masked implementation, each intermediate value is concealed by a random value that is called mask.
Masking Types
• Boolean masking (with xor ⊕): = ⊕
Mostly applied in symmetric cryptography i.e. AES
• Arithmetic masking (with + or ∙): = + or = ∙
Mostly applied in asymmetric cryptography

## Slide 15: Masking
Generate six independent random variables for the masks , , , , and
• 2 masks and for the Inverse S-box input and output
• 4 masks, , , for each row of the state for the input of Inverse MixColumns
• Calculate the masked InvS-box
InvSm(x ⊕ ) = InvS(x) ⊕
• Execute Inverse MixColumns for the masks , , , to create the output masks, ,

## Slide 16: Masking
Ciphertext
⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕
⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕
⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕
⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕ | ⊕ ⊕
RoundKey
⊕ | ⊕ | ⊕ | ⊕
⊕ | ⊕ | ⊕ | ⊕
⊕ | ⊕ | ⊕ | ⊕
⊕ | ⊕ | ⊕ | ⊕
Mask the ciphertext with [ xor xor , xor xor xor xor xor xor ]
Mask the round key with[ xor ]

## Slide 17: Masking
AddRoundKey
Inverse ShiftRows
Inverse SubBytes
AddRoundKey

## Slide 18: Masking
Inverse MixColumns
Remasking
Inverse ShiftRows
In the final round, skip Inverse MixColumns and Remasking. Remove the masks from the plaintext.
Remask with[⊕, ⊕, ⊕, ⊕]

## Slide 19: Masking
Inverse SubBytes
AddRoundKey
Inverse MixColumns
Remasking
Inverse
ShiftRows
Inverse SubBytes
AddRoundKey
Remove the masks from the plaintext

## Slide 20: Attack on Masking
Method: Second Order DPA
Idea: Using the two intermediate value
=()
Preprocessing: Use a combination function to combine points of the power trace (e.g. absolute difference, normalized product, … )
DPA attack: Perform a first-order DPA attack on the preprocessed power traces.
New sample size

## Slide 21: Attack on Masking
Method: Second Order DPA
First Mask Implementation Strategy
Result: Successful with first-order DPA attack 800 traces
(( )
= ( )
m | m | m | m
m | m | m | m
m | m | m | m
m | m | m | m
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
Inverse SubBytes
Reason: The result of two intermediate values
with the same mask would be unmasked

## Slide 22: Attack on Masking
Method: Second Order DPA
Second Mask Implementation Strategy
m | m | m | m
m | m | m | m
m | m | m | m
m | m | m | m
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
m’ | m’ | m’ | m’
Inverse SubBytes

## Slide 23: Attack on Masking

## Slide 24: Attack on Masking
) =

## Slide 25: Attack on Masking

## Slide 26: Attack on Masking
Normalized product combination:
Absolute difference combination:
Problems: Dealing with huge amount of traces
More effort for preprocessing
Result: Not successful with second-order DPA
(even with 10000 traces)

## Slide 27: Benchmark-Attack
Implementation | Time[s] | Yes/ No | No. Of Traces
Reference card | 70 | Yes | 170
Reference card | 6.3 | Yes | 800
Own Implementation(No Countermeasure) | 5.9 | Yes | 800
Own Implementation + Dummy Operations | 72 | Yes | 800
Own Implementation+ Shuffling | 183.47 | Yes | 10000
Own Implementation + Masking | N/A | No | 50000
Own Implementation + Masking m=m' | 11 | Yes | 800
Own Implementation + All Countermeasures | N/A | No | 50000

## Slide 28: True Random Number Generator
Create true random numbers using ADC readings
  Two floating inputs
  Differential mode with maximal gain (200x)
  Sequential readings only taking the LSB
Post processing with von Neumann corrector
New random seed after each decryption
  ADC readings do not affect AES Execution time
149 of 160 NIST tests passed [1]
  [1] Source: http://csrc.nist.gov/groups/ST/toolkit/rng/documentation_software.html

## Slide 29: Benchmark – Execution time
Measurement with TRNG and own PRNG
Chart: Execution time
| Reference card | Own implementation | OI + Dummy | OI + Shuffling | OI + Masking | OI + All
Datenreihe 1 | 4.4 | 2.7 | 14.1 | 7.2 | 9.6 | 25

## Slide 30: Benchmark – Memory usage
Compiled with code size optimization and own PRNG
Chart: Memory usage
| Own | D | S | M | D+S | S+M | D+M | D+S+M
Program | 6.0094 | 7.7219 | 7.6313 | 8.3938 | 7.775 | 9.5188 | 9.6 | 9.6625
Data | 50.575 | 52 | 51 | 61.75 | 52 | 62.05 | 63.05 | 63.05

## Slide 31: Conclusion
Lookup tables reduced the execution time of the AES to 2.7ms
Dummy Operations, Shuffling and Masking implemented successfully
Less than 10% of ROM and ~60% of SRAM used
Multiprocessing increased the script performance by a factor of upto 3x
Dummy Operations and Shuffling were attackable with adequate number of traces